## Slide 1
Carbon Pricing Exploration
October 23, 2019

## Slide 2: Outline
Project Overview
GCAM Collaboration
Next Steps

## Slide 3: Project Overview
This is a very small BETO-funded project
We envision this project producing the following:
  Develop new BSM results for a very small number of simulations with varying carbon price
  Comparisons of these simulations, harmonizing a very small number of parameters (just carbon price and petroleum prices to start). Compare with:
    GCAM-Global results for the United States
    GCAM-USA results?
  Analytic plan for future work
    Identify additional scenarios of highest priority
    Identify how additional parameters could be harmonized
  Plan for modifications to the BSM that would enhance carbon pricing analysis
We would like to complete this project in Q2
We are unlikely to publish at this point

## Slide 4: Selection Criteria for Top Priority Scenarios
Existing GCAM scenario (Global and USA, or just Global)
Links to literature (IPCC, EMF, IEA)
Specifications (proposed starting points in parentheses)
  SSPs (SSP2)
  Warming (1.5-2.5 degrees)
  Fossil Fuel Price ($100 - $300/barrel)
Can the GCAM team propose 4-10 scenarios that meet these criteria?

## Slide 5: List of GCAM parameters that can be used to inform BSM
Agricultural production levels and prices
Domestic energy consumption and prices
Domestic biofuel production levels
Domestic vehicle markets
International demand for biomass and bioenergy from the US
US energy imports
Carbon prices

## Slide 6: GCAM Data Needed
We think we should start by importing ONLY carbon price and petroleum price trajectories from GCAM-Global into BSM (Let’s discuss)
Can GCAM team provide these price trajectories for the identified scenarios?

## Slide 7: Additional Harmonization
Beyond carbon prices and petroleum prices, we would ultimately envision harmonizing the following:
  Numbers of vehicles
  Energy imports
  International demand for bioenergy
The following parameters would be compared across the models:
  Agricultural system metrics
  Bioenergy, including biofuels metrics
This would likely be left for future work

## Slide 8: BSM Parameters
Carbon price and petroleum price are represented by these parameters in the BSM
Details on definition and dimensionality of these parameters
Can we work together to get appropriate data from GCAM results for import into BSM?
Parameter’s name More things to harmonized | Dimension | Dimension
Prices of bioenergy, biofuels, petrol fuels |  | 
Oil Industry, AEO Reference Oil, $/bbl | Time series data 2015-2051 | Time series data 2015-2051
Oil Industry, AEO High Oil, $/bbl | Time series data 2015-2051 | Time series data 2015-2051
Oil Industry, AEO Low Oil, $/bbl | Time series data 2015-2051 | Time series data 2015-2051
Oil Industry, User Defined Oil, $/bbl | Time series data 2015-2051 | Time series data 2015-2051
Oil Industry, PoD PoP gasoline Offset (assumed spread between point of production (POP) and and point of distribution (PoD) gasoline prices), $/gal | Constant | Constant
Oil Industry, T2 per gallon transport cost to refinery, $/ gal | Constant | Constant
Oil Industry, C to R per gallon transport cost to refinery (Assumed average per-gallon cost of transporting fuel from conversion facility to refinery), $/ gal | Constant | Constant
Oil Industry, OC to R per gallon transport cost to refinery (Assumed average per-gallon cost of transporting fuel from conversion facility to refinery), $/ gal | Constant | Constant
Oil Industry, A to R per gallon transport cost to refinery(Assumed average per-gallon cost of transporting fuel from conversion facility to refinery), $/ gal | Constant | Constant
Oil Industry, SJ per gallon transport cost to refinery (Assumed average per-gallon cost of transporting fuel from conversion facility to refinery), $/ gal | Constant | Constant
Oil Industry, Additional RP rev per gal (Additional $/gal, by refinery product type, applied to different refinery end products produced by conversion pathways), $/gal | 1D array: gasoline, diesel, jet fuel, All Other | 1D array: gasoline, diesel, jet fuel, All Other
Oil Industry, RP crack spread intercepts (intercepts for linear equation that relates oil crude price to refinery product price), $/ gal | 1D array: gasoline, diesel, jet fuel, All Other | 1D array: gasoline, diesel, jet fuel, All Other
Oil Industry, Coproduct Price Spread (Multiplier applied to crude oil price per gallon to create price input for coproducts), unitless | 1D array: Primary, Co1, Co2 | 1D array: Primary, Co1, Co2
Inventory and Pricing, addl gas tax amt (Scenario driven additional gasoline tax tax in $/gal at the pump), $/gal | Constant | Constant
Inventory and Pricing, fuel excise tax, $/gal | Price per each region | Price per each region
Inventory and Pricing, B industrial price scenario (scenario input for price of industrial (non-bio-based) butanol), $/ gal | Constant | Constant
Ethanol Import Module, export tariff (Tariff associated with ethanol exports from US--time dependent scenario. Note stepwise graphical function), $/ gal | Time series data 2015-2051 | Time series data 2015-2051
Ethanol Import Module, import tariff (Tariff associated with ethanol imports into US-time dependent scenario. Note stepwise graphical function), $/ gal | Time series data 2015-2051 | Time series data 2015-2051
AHC, Price Increase Due to RINs (Scenario defining additional price impact resulting from renewable identification number (RIN)), $/ gal | 1D array: Time series data Algal Tech | 1D array: Time series data Algal Tech
OHC, Price Increase Due to RINs (Scenario defining additional price impact resulting from renewable identification number (RIN)), $/ gal | 1D array: Time series data Oil Crop Tech | 1D array: Time series data Oil Crop Tech
CHC, Price Increase Due to RINs (Scenario defining additional price impact resulting from renewable identification number (RIN)), $/ gal | 1D array: Time series data C to RR tech | 1D array: Time series data C to RR tech
CB, Price Increase Due to RINs (Scenario defining additional price impact resulting from renewable identification number (RIN)), $/ gal | 1D array: Time series data (no value in BSM) | 1D array: Time series data (no value in BSM)
CE, Price Increase Due to RINs (Scenario defining additional price impact resulting from renewable identification number (RIN)), $/ gal | 1D array: Time series data C to A tech | 1D array: Time series data C to A tech
SE, Price Increase Due to RINs (Scenario defining additional price impact resulting from renewable identification number (RIN)), $/ gal | 1D array: Time series data Gen | 1D array: Time series data Gen
SJ, Price Increase Due to RINs (Scenario defining additional price impact resulting from renewable identification number (RIN)), $/ gal | Time series data (no value in BSM) | Time series data (no value in BSM)
T2, Price Increase Due to RINs (Scenario defining additional price impact resulting from renewable identification number (RIN)), $/ gal | 1D array: Time series data T2Tech | 1D array: Time series data T2Tech
Carbon Price |  | 
Oil Industry, C tax scenario, $/tonnes | Time series data for Oil, T2, CHC, OC, Algae, SJ, CE, B, SE | 

## Slide 9
This work was authored [in part] by the National Renewable Energy Laboratory, operated by Alliance for Sustainable Energy, LLC, for the U.S. Department of Energy (DOE) under Contract No. DE-AC36-08GO28308. Funding provided by [applicable Department of Energy office and program office, e.g., U.S. Department of Energy Office of Energy Efficiency and Renewable Energy Solar Energy Technologies Office (spell out full office names; do not use initialisms/acronyms)]. The views expressed in the article do not necessarily represent the views of the DOE or the U.S. Government. The U.S. Government retains and the publisher, by accepting the article for publication, acknowledges that the U.S. Government retains a nonexclusive, paid-up, irrevocable, worldwide license to publish or reproduce the published form of this work, or allow others to do so, for U.S. Government purposes.
Insert the words “in part” if this work includes non-NREL authors.
.
Edit the red bracketed text as appropriate with the applicable DOE office(s) and program office(s) that sponsored the work and/or add other funding as needed. For non-EERE funding, see https://thesource.nrel.gov/publishing/disclaimers.html