## Slide 1: Sewage Sludge Economic Analysis
Alex Badgett, Emily Newes, Anelia Milbrandt
November 1, 2017
DRAFT – DO NOT CITE/DISTRIBUTE

## Slide 2: Modeling Overview

## Slide 3: Objectives
Characterize costs associated with treating and disposing of sewage sludge in the U.S.
Develop model that covers regional variability in sludge disposal alternatives
Model costs at different sized Publicly Owned Treatment Works (POTWs)
Create and analyze sewage sludge supply curves at national and regional levels
Run as-needed WTE model scenarios
DRAFT – DO NOT CITE/DISTRIBUTE

## Slide 4: Model Structure
DRAFT – DO NOT CITE/DISTRIBUTE
Primary & Secondary Treatment
Land Application
Hauling
Dewatering
Storage
Avoided Costs
Landfill
Added Costs
Incineration
Class A Biosolids
Long Term Storage
Sunk Costs
Model assumes that WTE technology is developed on-site at POTW

## Slide 5: National Sludge Supply Curves
DRAFT – DO NOT CITE/DISTRIBUTE
Differentiates supply curves for POTWs by daily plant inflow
Green curve suggests that large amounts of sludge are available at a fewer (less distributed) number of POTWs
Both curves model sludge as a negative cost WTE feedstock
Chart: $/Wet Ton

## Slide 6: Areas of Further Analysis

## Slide 7: Modeled Disposal Costs
DRAFT – DO NOT CITE/DISTRIBUTE
Cost per wet ton determined with 1985 EPA cost curves1 for different sludge disposal alternatives
Updated for inflation
Need to understand how these cost curves apply to modern POTW costs
Lacking real world data to calibrate model results
1EPA, “Handbook: Estimating Sludge Management Costs,” United States Environmental Protection Agency, 1985.

## Slide 8: Cost of Sludge Disposal Alternatives
POTW Size | Ag Land Application | Landfill | Incineration | Class A Biosolids | Long Term Storage
>10 and <50 MGD | $27.17 | $54.74 | $96.81 | $41.49 | $6.29
>50 MGD | $26.90 | $68.29 | $50.00 | $29.66 | $3.71
DRAFT – DO NOT CITE/DISTRIBUTE
No available data to validate the model average cost per wet ton shown above
Need a recent source for baseline cost estimation to validate our results with

## Slide 9: Sludge Disposal Alternatives
DRAFT – DO NOT CITE/DISTRIBUTE
Chart: Disposal Alternative Chosen by Model
| Class A | Landfill | Land Application | Incineration | Storage
 | 124 | 107 | 185 | 130 | 11
 | 0.22262 | 0.1921 | 0.33214 | 0.23339 | 0.019749
Prevalent sludge disposal option modeled by state
North East Biosolids and Residuals Association (NEBRA) survey data used to find the most likely disposal alternative2
National disposal alternative distribution as shown
2NEBRA, “A National Biosolids Regulation, Quality, End Use & Disposal Survey,” North East Biosolids and Residuals Association (NEBRA), 2007.

## Slide 10: Geospatial Disposal Cost
DRAFT – DO NOT CITE/DISTRIBUTE

## Slide 11: Dewatering and Storage
DRAFT – DO NOT CITE/DISTRIBUTE
Dewatering and storage are likely needed for sludge use as a WTE feedstock
Some POTWs already incorporate one or both, making them sunk costs
Their use varies regionally, however no known data exists to incorporate their cost into our modeling

## Slide 12: Dewatering and Storage National Supply Curves
DRAFT – DO NOT CITE/DISTRIBUTE
Chart: $/Wet Ton

## Slide 13: Thank you!