## Slide 1
Cooper basin
History of the project and learned lessons

## Slide 2
Initial conditions for development of
Australian EGS
Potential difficulties
Australian continent is under regional overthrust tectonic stress
1
Favorable factors
Extent of granitic basement with high heat flow due to radioactive decay
Abundance of data

## Slide 3
Hunter Valley
Development of EGS in Australia started in Hunter Valley
Boreholes at 300 m to 920m deep
Confirmation of geothermal anomaly on Australian continent
Stimulation of commercial interest in Australian’s hot dry rock
2
Hunter Valley EGS

## Slide 4
Cooper Basin
The interest shifted from Hunter Valley to Cooper Basin in 2002
Temperature approaches 250C at 4 km deep
Basin characteristics: overthrust tectonic stress, granitic basement, high heat flow because of radioactive activity
3

## Slide 5
Completed in 2004
Was targeted to intersect the reservoir at 4,310 m
Hit the reservoir at 4,325 m
Sidetrack in 2004
2005 – test of the well
Development of the geothermal resource in Cooper basin
Habanero 1
Completed in Oct, 2003
Total depth 4,421 m, intersected granite at 3,668 m
Was drilled into granite using a 1,740 kg/m3 mud till 4,139 m, from 4,139 m the well was drilled with lower mud density 1,410 kg/m3
Blow at 4,209 m
1,580 bbl (250 m3) - mud lost, 169 bbl (27 m3) - total influx
Nov.-Dec. 2003 – stimulation of the well, expansion of reservoir from 0.7 km2 to 3 km2
Sep. 2005 – stimulation of the well, expansion reservoir from 3 km2 to 4 km2
4
Habanero 2

## Slide 6
5
Test of the closed geothermal system
Delayed test in 2005
Apr.- June 2006 – Second sidetrack to reestablish connection between two wells

## Slide 7
6
Learned lessons at Cooper Basin
Buried radiogenic granite heat sources are ideal in this environment
Granite with relatively uniform - huge potential heat resource
???

## Slide 8
7
Learned lessons at Cooper Basin
Continuation

## Slide 9
Conclusion
Generalizations from EGS Field Testing

## Slide 10
Lessons Learned from Natural Hydrothermal Systems
Monitoring of acoustic emissions
Effect of rock-fluid interactions
Pumping the production well to get the high-pressure drops needed for high flow rates without increasing overall reservoir pressure seems to reduce the risk of short circuiting while producing at high rates
The wells needed to access the stimulated volume can be targeted and drilled into the fractures
Circulation for extended time periods without temperature drop is possible
Models are available for characterizing fractures and for managing the reservoir
Induced seismicity concerns
1